GP1200 Mounting

1, remove old sponsons and studs,

Set sponson to side of hull from 3-4 inches from rear and let it hang 1.5 inches down.

2, Mark the top three holes and drill ( If you use our screws make sure you have right drill bit 11/64). Usually slightly smaller then screw.

3,Add silicone heavy to back of sponsons.

4, Add screws and tighten. Wipe off excess silicon and Let dry 24hr.