Congratulations you have just purchased the best kit on the market. These kits have been thoroughly tested and designed to give you flawless results. When installed properly you will notice a dramatic increase in overall performance.

# Inland Jet water Injection

Important: Read These Instructions completely before attempting this install.

Warning: During Installation, Disconnect the battery cables. When disconnecting the battery, always remove the negative cable first and install it last.

Note:

Before installing the injection kit the crafts exhaust and water system must be functioning properly. The additional water supplied to the exhaust system by the injection kit is not intended to replace the original water system but to enhance it.

Note: Ultra owners need to go up in prop size. Call for recommendations.

## Remote mount

- Locate a position on the Exhausts head pipe where a hole can be drilled and tapped without entering the water jacket .

- On all other models normally, the best location to drill the hole is at the base of the head pipe where it attaches to the exhaust manifold(don’t go into jacket).

- Use a .250 (d) drill bit and drill the hole using extreme caution not to enter the water jacket.

- Thread the hole using a 1/16 NPT pipe tap. Install the spray nozzle so that the water will spray in the direction of the exhaust gases (up).

- Mount the solenoid on the hull in a position away from direct engine heat sources. Connect a hose from the spray fitting to the solenoid and then from the solenoid to the main water feed line to the engine. When plumbing the system, it is recommended that a water filter be installed on the water feed line to prevent clogging of the spray nozzle.

NOTE: It is recommended that the spray nozzle be periodically checked to ensure that the spray orifice is not obstructed or clogged.

Wiring

Red: connects to positive terminal (+) side on battery.

Black: Attaches to ground stud or battery negative (-) terminal.

Long white and Red/blk: Connect to solenoid.

Yellow: Inductive Pickup. It connects directly to a spark plug wire with zip tie.

.

Caution: Do not mount near ignition coil or plug wires (keep grease on jumpers and fuses.

Programming

The activation point where the water turns on and off is easily adjusted with the built-in selector switch. The switch is set at the factory with the basic curve.

Table A –Jumper 1&2    on                                   Amount of water

1,500       RPM                 Water                                          ON

5,200       RPM                 Buzz 1                                        5/8

5,300       RPM                 Buzz 2                                        4/8

5,400       RPM                 Buzz 3                                        3/8

5,500       RPM                 Buzz 4                                 2/8

5,600       RPM                 Water                                         OFF

Table B – Jumper 1 On                                         Amount of water

1,500       RPM                  Water                                          ON

5,300       RPM                  Buzz 1                                         5/8

5,400       RPM                  Buzz 2                                         4/8

5,500       RPM                  Buzz 3                                         3/8

5,600       RPM                  Buzz 4                                         2/8

5,700       RPM                  Water                                          OFF

Table C – Jumper 2 on                                          Amount of water

1,500       RPM                  Water                                           ON

5,400       RPM                  Buzz 1                                          5/8

5,500       RPM                  Buzz 2                                          4/8

5,600       RPM                  Buzz 3                                          3/8

5,700       RPM                  Buzz 4                                          2/8

5,800       RPM                  Water                                           OFF

Table D – Jumpers   OFF                                      Amount of water

1,500       RPM                  Water                                           ON

5,500       RPM                   Buzz 1                                         5/8

5,600       RPM                   Buzz 2                                         4/8

5,700       RPM                   Buzz 3                                         3/8

5,800       RPM                   Buzz 4                                         2/8

5,900       RPM                   Water                                          OFF

909-899-7070